## Slide 1
Unit 2: Technology Systems
Lesson 5 — Inside the Computer
How do the components inside a computer work together?
Motherboard • CPU • RAM • ROM • Buses • Cooling • Storage

## Slide 2
DO NOW — Retrieval Starter
Starter
Unit 2: Technology Systems • Lesson 5 • 2
1. What does LAN stand for?
2. What does WAN stand for?
3. Which technology would normally connect wireless earbuds to a phone?
4. What does UTP stand for?
5. Which cable transfers data using light?
6. Give one benefit of Wi-Fi.
No notes • 5 minutes

## Slide 3
Retrieval Answers
Starter
Unit 2: Technology Systems • Lesson 5 • 3
1. Local Area Network
2. Wide Area Network
3. Bluetooth
4. Unshielded Twisted Pair
5. Optical fibre
6. Examples: mobility, convenience, no physical network cable to the device.
Self-mark your answers.

## Slide 4
Today's Learning Objectives
Objectives
Unit 2: Technology Systems • Lesson 5 • 4
Identify important components inside a computer.
Explain the purpose of the motherboard and CPU.
Describe the ALU, Control Unit and registers.
Explain RAM and ROM.
Explain what a bus does.
Identify graphics, sound and video hardware.
Explain why computers need cooling.
Identify different types of storage.

## Slide 5
What's Inside a Computer?
Inside
Unit 2: Technology Systems • Lesson 5 • 5
A computer contains many components that work together.
Important components include: motherboard, CPU, RAM, ROM, storage, graphics hardware and cooling components.
Together they allow a computer to input, process, store and output data.
INPUT → PROCESS → STORE → OUTPUT

## Slide 6
Activity 1 — Component Challenge
Activity
Unit 2: Technology Systems • Lesson 5 • 6
60-SECOND CHALLENGE
Write down as many internal computer components as you can.
Next to any component you know, write its job.
Example: CPU — processes instructions.
1 point = correct component • +1 point = correct job

## Slide 7
The Motherboard
Components
Unit 2: Technology Systems • Lesson 5 • 7
MOTHERBOARD
The motherboard is the main printed circuit board (PCB) inside the computer.
Components such as the CPU, RAM, storage connections and expansion hardware connect to or communicate through it.
It provides the main connections that allow internal components to work together.
Remember: Motherboard = main circuit board connecting the computer's components.

## Slide 8
Motherboard — Quick Check
Activity
Unit 2: Technology Systems • Lesson 5 • 8
A. It permanently stores all user files.
B. It is the main circuit board that connects computer components.
C. It displays images on the monitor.
D. It only provides power to the CPU.
Which statement best describes a motherboard?
Answer: B • Now name TWO components that connect to it.

## Slide 9
What is the CPU?
CPU
Unit 2: Technology Systems • Lesson 5 • 9
CPU — Central Processing Unit
The CPU processes instructions and data.
It controls and carries out many instructions required by programs.
Three important parts associated with the CPU are the ALU, Control Unit and registers.

## Slide 10
Inside the CPU
CPU
Unit 2: Technology Systems • Lesson 5 • 10
ALU
CONTROL UNIT
REGISTERS
Performs calculations and logical operations. Example: 10 + 5 or comparing values.
Controls and coordinates processing and the execution of instructions.
Very small, very fast temporary storage locations inside the CPU.
Memory trick: ALU = Calculate • CU = Control • Registers = Hold

## Slide 11
Activity 2 — Match the CPU Part
Activity
Unit 2: Technology Systems • Lesson 5 • 11
Choose: ALU | CONTROL UNIT | REGISTERS
1. Performs calculations.
2. Temporarily holds information required immediately by the CPU.
3. Controls and coordinates processing.
4. Performs logical comparisons.
5. Very small and fast storage inside the CPU.
Challenge: Which component are all three found inside?

## Slide 12
CPU Activity — Answers
Activity
Unit 2: Technology Systems • Lesson 5 • 12
1 → ALU
2 → Registers
3 → Control Unit
4 → ALU
5 → Registers
All three are associated with the CPU.
Quick fire: Which calculates? Which controls? Which holds?

## Slide 13
What is RAM?
Memory
Unit 2: Technology Systems • Lesson 5 • 13
RAM — Random Access Memory
RAM stores programs and data that the computer is currently using.
Examples: an open document, a running application or an open browser.
RAM is volatile — its contents are lost when power is removed.
Remember: RAM = temporary working memory

## Slide 14
What is ROM?
Memory
Unit 2: Technology Systems • Lesson 5 • 14
ROM — Read Only Memory
ROM is non-volatile memory.
It retains its contents when the computer is switched off.
ROM can hold instructions or data needed by the computer system.
RAM loses contents without power • ROM retains contents without power

## Slide 15
RAM vs ROM
Memory
Unit 2: Technology Systems • Lesson 5 • 15
Feature | RAM | ROM
Full name | Random Access Memory | Read Only Memory
Purpose | Working memory | Persistent system instructions/data
Power | Volatile | Non-volatile
When power is removed | Contents lost | Contents retained
Typical use | Active programs/data | System / firmware purposes
Exam keyword: VOLATILE vs NON-VOLATILE

## Slide 16
Activity 3 — RAM or ROM?
Activity
Unit 2: Technology Systems • Lesson 5 • 16
Write RAM or ROM.
1. Stores data/programs currently being used.
2. Volatile.
3. Retains its contents when power is removed.
4. Random Access Memory.
5. Non-volatile.
6. Read Only Memory.
Challenge: Explain ONE difference between RAM and ROM in a full sentence.

## Slide 17
RAM or ROM — Answers
Activity
Unit 2: Technology Systems • Lesson 5 • 17
1. RAM
2. RAM
3. ROM
4. RAM
5. ROM
6. ROM
Strong comparison answer
RAM is volatile and loses its contents when power is removed, whereas ROM is non-volatile and retains its contents.

## Slide 18
What is a Bus?
Communication
Unit 2: Technology Systems • Lesson 5 • 18
The CPU, RAM and other components need to exchange information.
A bus provides a pathway that carries data/signals between internal components.
CPU ⇄ BUS ⇄ RAM
Remember: Bus = carries information between components

## Slide 19
Activity 4 — Complete the Journey
Activity
Unit 2: Technology Systems • Lesson 5 • 19
STORAGE
Program/data loaded into __________
Instructions processed by __________
Information moves between components using __________
Answers: RAM → CPU → Bus

## Slide 20
Graphics, Sound & Video Hardware
Hardware
Unit 2: Technology Systems • Lesson 5 • 20
GPU — Graphics Processing Unit
Graphics hardware processes graphical information.
It is especially useful for gaming, video, 3D graphics and CAD.
Sound hardware supports audio input/output and processing.
Video hardware supports video-related processing, capture or output depending on the system.
Different users need different hardware depending on their purpose.

## Slide 21
Activity 5 — Which Computer Needs More?
Activity
Unit 2: Technology Systems • Lesson 5 • 21
COMPUTER A — Reception PC
Emails • Documents • Web browsing
COMPUTER B — Design PC
3D modelling • Video editing • Graphics work
1. Which computer needs stronger graphics hardware?
2. Why?
3. Why might identical high-end graphics hardware be unnecessary for every basic office PC?
Discuss for 2 minutes, then write your answer.

## Slide 22
Why Do Computers Need Cooling?
Cooling
Unit 2: Technology Systems • Lesson 5 • 22
Components such as the CPU produce heat while operating.
Too much heat can affect performance, stability and component reliability.
Fans move air to help remove heat.
Heat sinks transfer heat away from a component and increase the surface area for heat to dissipate.
Fans and heat sinks are often used together.
CPU → HEAT SINK → AIRFLOW / FAN → HEAT REMOVED

## Slide 23
Activity 6 — Cooling Scenario
Activity
Unit 2: Technology Systems • Lesson 5 • 23
A computer is running a demanding task. The CPU becomes hot, but the cooling fan has stopped working.
1. What could happen to the CPU temperature?
2. How could excessive heat affect the computer?
3. Name TWO cooling components.
4. Challenge: Why might a more powerful computer require effective cooling?
4 minutes

## Slide 24
Storage Devices
Storage
Unit 2: Technology Systems • Lesson 5 • 24
Computers need storage for operating systems, applications, documents, photos, videos and other files.
Solid state storage — example: SSD.
Magnetic storage — example: HDD.
Optical storage — examples: CD / DVD.
We will compare their performance in more detail in Lesson 6.
Important: STORAGE is not the same as RAM.

## Slide 25
Activity 7 — Computer Technician Challenge
Main Activity
Unit 2: Technology Systems • Lesson 5 • 25
A customer asks: “What do the components inside my computer actually do?”
Complete a table with the component and its job:
Motherboard • CPU • ALU • Control Unit • Registers • RAM • ROM • Bus • GPU • Fan/heat sink • Storage
Use simple, complete sentences.
Example: RAM provides temporary working memory for programs and data currently being used.
10 minutes — use your lesson notes if needed

## Slide 26
Activity 8 — Spot the Mistakes
Activity
Unit 2: Technology Systems • Lesson 5 • 26
Student A: “RAM permanently stores all my files.”
Student B: “The ALU controls the whole computer.”
Student C: “ROM loses its contents when the power is switched off.”
Student D: “The bus is used to cool the CPU.”
Student E: “A GPU is mainly used to store documents.”
Correct each statement. Challenge: rewrite every sentence accurately.

## Slide 27
Independent Exam Practice
Assessment
Unit 2: Technology Systems • Lesson 5 • 27
Q1. State what CPU stands for. [1]
Q2. Name the part of the CPU that performs arithmetic and logical operations. [1]
Q3. State what RAM stands for. [1]
Q4. Explain one difference between RAM and ROM. [2]
Q5. Explain the purpose of a bus inside a computer. [2]
Q6. Explain why a computer requires cooling. [2]
Q7. Explain the purpose of the motherboard. [2]
Total: 11 marks • Work independently for 8–10 minutes

## Slide 28
Final Recap & Homework
Plenary
Unit 2: Technology Systems • Lesson 5 • 28
Main circuit board? → Motherboard
Processes instructions? → CPU
Calculations and logic? → ALU
Controls processing? → Control Unit
Small fast CPU storage? → Registers
Volatile working memory? → RAM
Non-volatile memory? → ROM
Carries information between components? → Bus
Processes graphics? → GPU
Cooling? → Fan / heat sink
HOMEWORK — 5–10 MINUTES
Match each description to: CPU • RAM • ROM • ALU • Motherboard • Bus 1. Performs calculations and logical operations. 2. Volatile working memory. 3. Main printed circuit board. 4. Processes instructions. 5. Non-volatile memory. 6. Carries information between components. Challenge: Explain ONE component in a full sentence.
Next lesson: Computer Performance & Storage